## Slide 1
Figure 1. Proposed mechanism of PBM-induced AVA vasodilation
PBM Irradiation (630–850 nm, 20–100 mW/cm²)
↓
Photon absorption by CcO / nitrosyl-Hb in dermal vessels
↓
NO release from endothelial stores (S-nitrosothiols)
↓
sGC activation → cGMP↑ → PKG activation
↓
AVA smooth muscle relaxation → AVA DILATION
↓
Parallel low-resistance pathways added to systemic circulation
↓
TPR reduction (estimated 5–10%)
↓
ΔMAP = −4.5 to −9 mmHg (clinically significant)
Fig. 1. Schematic of proposed causal chain from photobiomodulation to blood pressure reduction via AVA vasodilation. CcO = cytochrome c oxidase; Hb = hemoglobin; NO = nitric oxide; sGC = soluble guanylate cyclase; cGMP = cyclic guanosine monophosphate; PKG = protein kinase G; AVA = arteriovenous anastomosis; TPR = total peripheral resistance; MAP = mean arterial pressure.

## Slide 2
Table 1. Comparison of arteriovenous shunt-based blood pressure reduction strategies
Approach | Mechanism | BP reduction (SBP, mmHg) | Invasiveness | Evidence level
ROX Coupler (iliac AV fistula) | Surgically created fixed AV shunt | −26.9 | Invasive (catheter) | RCT (n=83)
AVACEN 100 (palm heating + neg. pressure) | Conductive heat + vacuum → AVA dilation | Under investigation | Non-invasive (stationary) | Pilot studies
Selective thermal stimulation (Diller, 2022) | Spinal heating → hypothalamic reflex → AVA dilation | Not yet reported | Non-invasive (bed-integrated) | POC (n=10)
PBM-AVA device (proposed) | PBM → NO release → AVA dilation → TPR↓ | Predicted: −5 to −10 | Non-invasive (wearable) | Hypothesis